void do_send(osjob_t* j)
{
    // Check if there is not a current TX/RX job running
    if (LMIC.opmode & OP_TXRXPEND)
   {
        Serial.println(F("OP_TXRXPEND, not sending"));
    }
    else
   {
        // Prepare upstream data transmission at the next possible time.
        LMIC_setTxData2(1, mydata, sizeof(mydata) - 1, 0);
        Serial.println(F("Packet queued"));
    }
    // Next TX is scheduled after TX_COMPLETE event.
}

- The function is defined with the name do_send, and it takes a pointer to an osjob_t structure as its argument. The osjob_t structure is used by the LMIC library to manage jobs and tasks, such as transmitting or receiving data.
- The function begins by checking whether there is a current transmission or reception job (OP_TXRXPEND) in progress. If there is, it prints a message to the serial console stating that a job is already pending, and it cannot send another message at this moment. This check ensures that you don't initiate multiple transmissions concurrently, which would violate LoRaWAN regulations.
- If there is no ongoing job (i.e., the if condition is not met), the function proceeds to prepare the data for upstream transmission.
- It calls the function LMIC_setTxData2 to set up the data transmission. The parameters for LMIC_setTxData2 are as follows:
  - 1: The first argument is the port number. This is a number between 1 and 223 that represents the logical port on the LoRaWAN packet. It helps the network server route the data to the appropriate application on the backend.
  - mydata: The second argument is a pointer to the data to be sent. In this case, it's the mydata array, which contains the payload "Hello, world!"
  - sizeof(mydata) - 1: The third argument is the size of the data to be sent. It calculates the size of the mydata array and subtracts 1 to exclude the null-terminating character at the end of the string.
  - 0: The fourth argument is the frame options, which is set to 0 in this case.
- After setting up the data for transmission, the function prints a message to the serial console, indicating that the packet is queued for transmission.
- The do_send function does not actually send the data immediately. Instead, it schedules the next transmission to occur after the EV_TXCOMPLETE event. This event is raised when the previous transmission is complete, including any waiting for receive windows. The actual transmission happens when this event occurs.
- Overall, the do_send function ensures that the LoRaWAN device is ready to send data and schedules the transmission in accordance with LoRaWAN duty cycle limitations, network settings, and the completion of previous transmissions. This approach helps maintain compliance with LoRaWAN regulations and efficient use of resources.

void loop()
{
    unsigned long now;
    now = millis();
    if ((now & 512) != 0)
   {
      digitalWrite(13, HIGH);
    }
    else
   {
      digitalWrite(13, LOW);
    }

    os_runloop_once();

}

in this void loop codes other than “os_runloop_once();” is for inbuild indicator led.which is using as a indicator to the transmission of data through lora.
unsigned long now;
    now = millis();
    if ((now & 512) != 0)
   {
      digitalWrite(13, HIGH);
    }
    else
   {
      digitalWrite(13, LOW);
    }
we can remove the code if we dont want led indication

const lmic_pinmap lmic_pins = {
    .nss = 8, // chip select on feather (rf95module) CS
    .rxtx = LMIC_UNUSED_PIN,
    .rst = 4, // reset pin
    .dio = {6, 5, LMIC_UNUSED_PIN}, // assumes external jumpers [feather_lora_jumper]

  this section is using to define pin of arduino pro mini used for connecting rfm95 lora module.we need to change the pins based on our connection.